## Slide 1: Vehicle stability control using Sideslip Control
Vehicle Dynamics & Control - R047017
By Group 5:
Neeraja Bhide (5495601)
Pavan Prasad H.G. (5508053)
Paul Kartoidjojo (4480961)
Anand Srikrishna (5306485)

## Slide 2: Table of contents
Motivation
Problem Statement
Control Strategies
Vehicle Validation Model
Simulation & Results
Conclusion
Future Work

## Slide 3: Motivation

## Slide 4: Motivation:
Vehicle sideslip angle is a major indicator of dynamics stability for ground vehicles. [1]
Sideslip angle can provide important information for direction stability control systems. [2]
It is immeasurable with commercially-available sensors.
[1] - Jizheng Liu et al. Sideslip Angle Estimation of Ground Vehicles: A Comparative Study
[2] - Federico Cheli et al. A methodology for vehicle sideslip angle identification: comparison with experimental data

## Slide 5: Problem Statement

## Slide 6: Problem Statement
“ Vehicle stability control from body Sideslip Control using Direct Yaw Moment Control”

## Slide 7: Control Strategies

## Slide 8: Reference Generator
Reference yaw rate (rd,ref) is generated from the steering wheel angle δ input using the bicycle model second-order transfer function

## Slide 9: Direct Yaw moment Control
Error Yaw rate is fed into the controller.
LQR controller is designed considering the control input dMZ
Mz = Klqr (u)(rd,ref − r)

## Slide 10: Control Strategies
Direct Yaw Moment Control (DYC) with PD Control of Sideslip angle
Direct Yaw Moment Control (DYC) with reference correction
Direct Yaw Moment Control (DYC) with the saturation of yaw rate
Notes: \

## Slide 11: PD Control of Sideslip angle
Additional yaw moment ∆Mz, computed using PD control of sideslip angle is added to Mz.
Controller is activated only on the conditions : β ≥ 5 deg and ≥ 10 deg/s

## Slide 12: With reference correction
Adjustments are adopted to reference generator
After trials, k1 is set as 0.85 and k2 is set as 1

## Slide 13: With yaw rate saturation
Limitation is introduced on the maximum lateral acceleration and maximum sideslip angle
Reference sideslip angle is assigned as
The maximum yaw rate is thus obtained as
Steady state yaw rate is assigned with

## Slide 14: Vehicle Validation Model

## Slide 15: Vehicle validation model
Linear Bicycle model
Notes: \

## Slide 16: Simulation & Results

## Slide 17: Simulation and Results
Notes: \

## Slide 18: Conclusions

## Slide 19: Conclusions
Notes: \

## Slide 20: Future work

## Slide 21: Future Work
Notes: \

## Slide 22: Thank you for your attention
Neeraja Bhide (5495601)
Pavan Prasad H.G. (5508053)
Paul Kartoidjojo (4480961)
Anand Srikrishna (5306485)